## Slide 1
Mastering Network Packet Crafting with Scapy
From Ethernet Frames to Custom Protocols · Building Professional Network Analysis & Security Tools in Python

## Slide 2
Learning Roadmap
• Module 1 — Foundations: Scapy architecture, packet stacking, PCAP I/O
• Module 2 — Layer 2 & 3: Ethernet, ARP, ICMP, ping, traceroute, fragmentation
• Module 3 — Transport Layer: TCP/UDP headers, three-way handshake, port scanning, banner grabbing
• Module 4 — Sniffing & Analysis: Live capture, BPF filters, HTTP/DNS/DHCP dissection, traffic dashboards
• Module 5 — Security Testing: ARP spoofing detection, DNS/DHCP monitoring, packet replay
• Module 6 — Performance & Custom Protocols: Async processing, high-performance capture, custom dissectors
• Capstone — Enterprise Network Security Toolkit

## Slide 3
Prerequisites
• Python 3.8+ — intermediate level (functions, classes, comprehensions)
• Linux basics — command line, sudo, package management
• TCP/IP working knowledge — IP addressing, ports, routing
• Recommended: Wireshark, familiarity with ping/traceroute
• All tools are free and open source

## Slide 4
MODULE 01
Foundations of Packet Crafting
Install & verify Scapy environment
Understand the '/' stacking operator (Russian nesting dolls model)
Build and inspect multi-layer packets
Read/write PCAP files with rdpcap / wrpcap / PcapReader
Build a PCAP analyzer with protocol distribution & JSON export

## Slide 5
Packet Stacking Model
• Think of it as Russian nesting dolls or onion layers
• Outside layer → Inside layer: Ether() / IP() / TCP() / Raw()
• Access layers: packet[IP].src, packet[TCP].dport
• Inspect: show(), summary(), show2(), hexdump(), command()
• show2() displays auto-calculated checksums
ping = Ether() / IP(dst="8.8.8.8") / ICMP() http = Ether() / IP(dst="192.168.1.1") / TCP(dport=80) / Raw(b"GET / HTTP/1.1\r\n\r\n") if ping.haslayer(TCP): print(ping[TCP].dport)

## Slide 6
MODULE 02
Layer 2 & Layer 3 Operations
Ethernet frame construction — unicast, broadcast, multicast
VLAN tagging with 802.1Q (Dot1Q) and Q-in-Q
ARP request/reply mechanics and scanner implementation
Custom ping utility with statistics
Traceroute from scratch using TTL manipulation
IP fragmentation and reassembly

## Slide 7
ARP & ICMP Essentials
• ARP maps IP → MAC; requests are broadcast, replies are unicast
• ARP scanning is more reliable than ping (works when ICMP is blocked)
• ICMP Echo Request (type 8) / Echo Reply (type 0) — the ping packet
• Traceroute sends packets with increasing TTL; routers return Time Exceeded (type 11)
• Use srp() for Layer 2 send/receive; sr1() for Layer 3
arp_req = Ether(dst="ff:ff:ff:ff:ff:ff") / ARP(op=1, pdst="192.168.1.1") reply = srp1(arp_req, timeout=3) ping = IP(dst="8.8.8.8", ttl=64) / ICMP(type=8, id=12345, seq=1) reply = sr1(ping, timeout=3)

## Slide 8
MODULE 03
Transport Layer Protocols & Reconnaissance
TCP vs UDP — connection-oriented vs connectionless
TCP header flags: SYN, ACK, FIN, RST, PSH, URG
Three-way handshake and four-way termination in Scapy
SYN (half-open), Connect, FIN, NULL, XMAS port scanning
Multi-threaded scanning with rate limiting
Service detection and banner grabbing

## Slide 9
Port Scanning Techniques
• SYN Scan — stealthy half-open; send SYN, check for SYN-ACK
• Connect Scan — full handshake; no root required but noisier
• UDP Scan — ICMP Port Unreachable = closed; no response = open/filtered
• FIN/NULL/XMAS — stealth scans for systems not following RFC 793
• Always send RST after SYN-ACK to close half-open connections
packet = IP(dst=target) / TCP(dport=port, flags="S") reply = sr1(packet, timeout=2) if reply and reply[TCP].flags & 0x12: # SYN-ACK send(IP(dst=target)/TCP(dport=port, flags="R")) return "open"

## Slide 10
MODULE 04
Packet Sniffing & Traffic Analysis
Real-time capture with sniff() — prn callback, BPF filters, timeout
Kernel-level BPF filtering for performance
Protocol-specific analysis: HTTP, DNS, DHCP, ARP, TLS
Traffic statistics engine — protocol distribution, top talkers, flows
DNS monitor with caching and suspicious domain detection
Live dashboard with packet/byte rates

## Slide 11
Sniffing & BPF Filters
• sniff(filter="tcp port 80", prn=callback, store=False)
• store=False for memory efficiency on long captures
• BPF filters: host, net, port, src/dst, protocol, combined with and/or
• Promiscuous mode captures all traffic on the wire
• Use PcapReader for large files; rdpcap for small complete analysis
sniff(filter="tcp port 80 and host 192.168.1.100", prn=lambda p: print(p.summary()), count=100, store=False)

## Slide 12
MODULE 05
Active Network Manipulation & Security Testing
ARP spoofing detection — IP-MAC mapping changes, duplicate IPs
Packet injection framework with authorization & rate limiting
Packet replay from PCAP with safety controls
DNS security monitoring — tunneling, cache poisoning, DGA detection
DHCP rogue server detection via DORA sequence tracking
All techniques for authorized lab environments only

## Slide 13
Security Monitoring
• ARP spoofing: monitor for MAC changes on same IP, gratuitous ARP anomalies
• DNS: flag long domains (>50 chars), random subdomains, base64 strings, dynamic DNS
• DHCP: track DORA sequence, compare server IPs against authorized list
• Always implement authorization whitelists and rate limits
• Log all activity for audit trails
if src_ip in ip_mac_map: if ip_mac_map[src_ip] != src_mac: alert(f"MAC change: {src_ip} {old} -> {new}") if len(domain) > 50 or re.search(r"[a-z0-9]{8,}\.", domain): alert(f"Suspicious DNS: {domain}")

## Slide 14
MODULE 06
Automation, Performance & Custom Protocols
Producer-consumer pattern for high-performance capture
Multi-threaded and asyncio-based processing pipelines
Efficient data structures: deques, bloom filters, batch processing
Custom protocol dissectors with Packet class and field bindings
Protocol fuzzing for robustness testing
Capstone: integrated Network Security Toolkit CLI

## Slide 15
Custom Protocols & Fuzzing
• Extend Scapy with Packet subclass and fields_desc
• Bind layers with bind_layers(IP, MyProtocol, proto=250)
• Field types: ByteField, ShortField, IntField, IPField, MACField, StrLenField
• Fuzzing: mutate fields with bit flips, random values, boundary tests
• Test dissection robustness against malformed packets
class MyProtocol(Packet): name = "MyProtocol" fields_desc = [ ByteField("version", 1), ShortField("length", 0), IntField("sequence", 0) ] bind_layers(IP, MyProtocol, proto=250)

## Slide 16
Capstone: Network Security Toolkit
• Integrated CLI: nstool scan | sniff | analyze | protocol
• Discovery Engines — ARP scanner, ping suite, traceroute, port scanner
• Analysis Engines — PCAP reader, protocol dissector, custom parser
• Monitoring Pipelines — live sniffer, BPF filtering, flow reassembly, anomaly detection
• Plugin framework for extensibility
• Export & logging, reporting engine, visualization

## Slide 17
Ethics & Responsible Use
• Never test on a system or network without explicit written authorization
• CFAA (US), Computer Misuse Act (UK), GDPR (EU) — know the legal framework
• Practice in isolated lab environments only
• Build defensive tools, not offensive weapons
• Disclose responsibly, stay within scope

## Slide 18
Thank You
Mastering Network Packet Crafting with Scapy · Questions?