## Slide 1
Demystifying Network Protocols
From Ethernet Frames to HTTP/3

## Slide 2
00
Introduction

## Slide 3
Why This Matters
Protocols are hidden behind APIs, libraries, and OS abstractions
Most tutorials focus on theory or configuration—not how they work
The gap between 'what' and 'how' limits your ability to debug
Understanding the full stack is essential for building distributed systems
Target: Software Developers, DevOps, Cloud Engineers, Security Pros, Students

## Slide 4
The Three Pillars
Observe — Capture real traffic with Wireshark, tcpdump, tshark
Build — Write Python/Node.js socket applications from scratch
Troubleshoot — Diagnose DNS failures, packet loss, TLS errors, MTU issues
Every concept is reinforced with hands-on labs.

## Slide 5
Toolkit
Wireshark / tshark — GUI and CLI packet analysis
tcpdump — Server-side capture
ping / traceroute / dig — Connectivity and path mapping
curl / openssl — HTTP and TLS debugging
netstat / ss / ip — Connection and routing inspection
Python socket / Node.js net,dgram — Low-level programming

## Slide 6
01
Local Link Layer

## Slide 7
OSI vs TCP/IP
OSI 7-Layer Model: Physical → Data Link → Network → Transport → Session → Presentation → Application
TCP/IP 4-Layer Model: Link → Internet → Transport → Application
Encapsulation: Each layer wraps data with its own header as it moves down
Decapsulation: Headers are stripped as data moves up at the destination

## Slide 8
Encapsulation Flow
[ Application Data ]
↓
[ TCP Header | App Data ]
↓
[ IP Header | TCP | App Data ]
↓
[ Eth Header | IP | TCP | App Data ]
↓
[ 1s and 0s on the wire ]

## Slide 9
Ethernet & MAC
Ethernet frame: Preamble + Dst MAC + Src MAC + EtherType + Payload + FCS
MAC address: 48-bit hardware address (OUI + NIC-specific)
Unicast → one device | Broadcast → all devices | Multicast → group
Switches learn MAC-to-port mappings; flood unknown destinations

## Slide 10
ARP: Address Resolution
Problem: IP addresses (Layer 3) need MAC addresses (Layer 2) for local delivery
ARP Request: Broadcast 'Who has this IP?'
ARP Reply: Unicast 'This IP is at this MAC'
ARP cache stores mappings for 1–5 minutes to reduce broadcast traffic
Gratuitous ARP: Device announces its own IP/MAC to detect conflicts
ARP spoofing attacks poison caches to redirect traffic—mitigate with DAI.

## Slide 11
DHCP: Auto-Configuration
DORA: Discover → Offer → Request → Acknowledge
DHCPDISCOVER (broadcast) → DHCPOFFER (unicast) → DHCPREQUEST (broadcast) → DHCPACK
Lease renewal at 50% (T1) and 87.5% (T2) of lease time
Provides IP, subnet mask, gateway, DNS servers, domain name, lease duration
Without DHCP, every device would need manual static configuration.

## Slide 12
02
Network Layer

## Slide 13
IPv4 Fundamentals
32-bit address space: ~4.3 billion unique addresses
Header: Version, IHL, TOS, Total Length, ID, Flags, Fragment Offset, TTL, Protocol, Checksum, Src IP, Dst IP
TTL decrements per hop; packet discarded at 0 (prevents loops)
Protocol field: 1=ICMP, 6=TCP, 17=UDP

## Slide 14
Addressing & Subnetting
CIDR notation: 192.168.1.0/24 means first 24 bits = network
Private ranges: 10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
NAT allows multiple private devices to share one public IP
Subnetting divides networks; longest prefix match determines route

## Slide 15
IPv6
128-bit addresses: 340 undecillion addresses—no more exhaustion
Simplified 40-byte fixed header; no fragmentation in routers
SLAAC: Stateless auto-configuration without DHCP server
Types: Global Unicast (2000::/3), Link-Local (fe80::/10), Unique Local (fc00::/7)

## Slide 16
ICMP & Diagnostics
Type 0/8: Echo Reply / Echo Request (ping)
Type 3: Destination Unreachable (network, host, port, fragmentation needed)
Type 11: Time Exceeded (traceroute exploits TTL expiration)
Path MTU Discovery uses ICMP to find maximum packet size without fragmentation

## Slide 17
03
Transport Layer

## Slide 18
UDP: Speed Over Reliability
Connectionless, unreliable, minimal 8-byte header
No handshake, no sequencing, no flow control
Use cases: DNS, VoIP, video streaming, online gaming, SNMP
Checksum optional in IPv4, mandatory in IPv6
When your application can tolerate loss but not latency, choose UDP.

## Slide 19
TCP: Reliability by Design
Connection-oriented: three-way handshake (SYN → SYN-ACK → ACK)
Reliable delivery via sequence numbers, acknowledgments, retransmissions
Flow control: sliding window prevents sender from overwhelming receiver
Congestion control: slow start, congestion avoidance, fast retransmit/recovery

## Slide 20
TCP Three-Way Handshake
Client Server
| |
| 1. SYN (seq=x) |
| 'I want to connect' |
|----------------------------->|
| |
| 2. SYN-ACK (seq=y, ack=x+1) |
| 'OK, I received x' |
|<-----------------------------|
| |
| 3. ACK (seq=x+1, ack=y+1) |
| 'Connection established' |
|----------------------------->|
| |
| [ESTABLISHED] |

## Slide 21
TCP Connection Teardown
Four-way termination: FIN → ACK → FIN → ACK
TCP is full-duplex; both sides must independently close
TIME_WAIT: Client waits 2×MSL before fully closing
RST flag aborts connection immediately without graceful close

## Slide 22
04
Application Layer

## Slide 23
DNS: The Internet's Phonebook
Hierarchical: Root → TLD (.com) → Authoritative (example.com)
Recursive resolver caches results to speed up queries
A/AAAA: IPv4/IPv6 address | CNAME: alias | MX: mail server
TXT: verification strings | NS: name server | PTR: reverse lookup

## Slide 24
HTTP: Request / Response
Methods: GET, POST, PUT, DELETE, PATCH, HEAD, OPTIONS
Idempotent vs Safe: GET is both; POST is neither
Status codes: 2xx success, 3xx redirect, 4xx client error, 5xx server error
Headers, cookies, and sessions manage state across requests

## Slide 25
HTTP/2 & HTTP/3
HTTP/2: Binary, multiplexed streams, server push, HPACK header compression
HTTP/3: Runs over QUIC (UDP) instead of TCP
QUIC eliminates head-of-line blocking with independent streams
0-RTT resumption and connection migration (IP changes don't break the connection)
QUIC combines TLS 1.3 + TCP reliability + HTTP/2 multiplexing over UDP.

## Slide 26
Email Protocols
SMTP (port 25/587/465): Sending email via HELO, MAIL FROM, RCPT TO, DATA
POP3 (port 110/995): Download-and-delete; single-device focused
IMAP (port 143/993): Server-side storage; multi-device sync; folders
Modern email relies on SPF, DKIM, and DMARC for authentication

## Slide 27
05
Security & Modern Protocols

## Slide 28
Encryption Primitives
Symmetric: AES, ChaCha20 — same key encrypts and decrypts; fast for bulk data
Asymmetric: RSA, ECC — public key encrypts, private key decrypts; slow but secure
Hybrid TLS: Asymmetric handshake establishes shared secret, then symmetric bulk encryption
Digital signatures prove authenticity without revealing the private key

## Slide 29
TLS 1.3 Handshake
1-RTT handshake (vs 2-RTT in TLS 1.2)
Mandatory Perfect Forward Secrecy via ephemeral Diffie-Hellman
Even if long-term private key is compromised, past sessions remain secure
0-RTT resumption for returning clients—subsequent connections are instant

## Slide 30
Certificate Validation
Chain verification: Leaf → Intermediate CA → Root CA
Validity period, domain name matching (CN + SAN), key usage checks
Revocation: OCSP and CRL ensure compromised certs are rejected
All checks must pass or the browser shows an untrusted connection warning

## Slide 31
Packet Analysis with Wireshark
Capture filters (BPF): host, port, net, protocol, boolean logic
Display filters: tcp.flags.syn==1, http.request.method=='GET', dns.qry.name
Follow TCP/HTTP/TLS streams to reconstruct conversations
Decrypt TLS traffic with SSLKEYLOGFILE for deep inspection

## Slide 32
06
Conclusion

## Slide 33
The Complete Stack
┌─────────────────────────────────────┐
│ Application DNS, HTTP, SMTP │
├─────────────────────────────────────┤
│ Security TLS, HTTP/3, QUIC │
├─────────────────────────────────────┤
│ Transport TCP, UDP, Sockets │
├─────────────────────────────────────┤
│ Network IPv4, IPv6, Routing │
├─────────────────────────────────────┤
│ Link Ethernet, ARP, DHCP │
├─────────────────────────────────────┤
│ Physical Copper, Fiber, WiFi │
└─────────────────────────────────────┘

## Slide 34
What You Can Now Do
Build: TCP/UDP servers, HTTP clients, DNS tools, SMTP clients, SNMP monitors
Diagnose: Packet loss, latency, DNS failures, TLS handshake errors, MTU issues
Secure: Implement TLS clients, validate certificates, decrypt traffic
Optimize: Choose TCP vs UDP vs QUIC based on application requirements

## Slide 35
Next Steps
Deepen: SDN, NFV, BGP, MPLS, network automation
Certify: CCNA/CCNP, AWS/Azure networking, Network+
Build: Monitoring dashboards, packet analyzers, VPN servers, load balancers
Share: Write, present, contribute to open-source networking projects

## Slide 36
Thank You
Questions?